## Slide 1: Machine Vision: From Raw Pixels to
Autonomous Decisions
The mathematica[ foundations of Convolution, Filtering, and Image Restoration.

## Slide 2: Robots Do Not Understand Pictures. They Process Arrays of Numbers.
HUMAN PERCEPTION ROBOT PERCEPTION
Insight: Before a robot can make a decision, it must bridge the gap between noisy sensor input and clean data. These techniques clean, enhance, and connect images befone decisions ane made.

## Slide 3: Convolution is the Atomic Unit of Image Processing
Engineering Editorial
Filter / Kernel
Input Image
(Pixels)
Output
Feature Map
DEFINITION:
A mathematical operation that applies a small matrix (Kernel) to an 1mage to mod1fy 1t .
WHY IT MATTERS: The
underlying mechanism
for blurring, sharpening,
and edge detection.

## Slide 4: The Mechanics of the Sliding Window
STEP-BY-STEP:
1. PLACE: Align the kennel
over the image pixels.
FIULTIPLY: MuTtip1y
overlapping pixel values
with kernel values.
ADD: Sum the results.
OUTPUT: Place final value
in the new image array.
NOTE: Example shorn : Average Filter (Blur). By
averaging
inage is
neighbors, the
smoothed .

## Slide 5
Filtering Transforms Chaos into Manageable Signals
Filtering modifies an
1nage by spec1f1cal1y
enhanc1ng or suppress1ng
certain features . It is implemented mathematically using sonvolution.
Remove Noise (Grainy Data)
Enhance Edges
(Boundar1es)
Snooth Images
(Pre-processing)
Noisy Input
Raw Feed
Filten
(Convolution)
Clean Signal
Filtered Feed

## Slide 6: The Toolkit: Low-Pass vs. High-Pass Filtering
Low-Pass Filter (Gaussian Blur)
Function: Removes noise, smooths image. keeps low-frequency data.
High-Pass Filter (Laplacian)
Function: Enhances edges, highlights boundaries. Heeps high-frequency changes.
Crucial for Robotics: Low-pass cleans the view; High-pass finds the obstacles.

## Slide 7: Image Enhancement: Optimizing for Interpretation
Goal: Improving visual quality for better interpretation.
hey Characteristic: Subjective. Depends on human or robot needs,
not a ground truth .
Raw, Low Contrast (N1ght V1sion)
Brightness
Adjustment +
Contrast Stretch1ng
Enhanced for Navigation
Robotic Application: Increasing brightness in dark environments allows
navigation algorithms to function.

## Slide 8: Image Restoration: Recovering the Original Truth
known errors.
Degraded Image (Notion Blur)
Robotic Application: Removing
Inverse F1Iter1ng /
Noise Modeling
Restored Image (Sharp, Scannable)
motion blur aTTows for accurate localization
even when the robot is moving at speed.

## Slide 9: The Critical Distinction: Enhancement vs. Restoration

## Slide 10: Histogram Processing: Decoding Light Distribution
A histogram maps the distribution of pixel intensity values. It is a diagnostic tool for robot vision.
Pixel Intensity Histogram
0
UndereKposed
/ Low Contrast
b4
128
Pixel Intensity (O=Black, 255=White)
192
Corresponding Dark Inage
255

## Slide 11: Automating Clarity with Histogram Equalization
Raw Input
0
BE 100 1S0 200 2SS
Algorithm: Redistribute Intensities
Equalized Output
0
H
100 150 200 25S
Essential for outdoor robots dealing with variable sunlight and deep shadows.

## Slide 12: The Pipeline of Perception
Input Image (Raw Data)
Convolut1on + Filtering (Noise Removal, Edge Setup)
Image Enhancement / Restoration
(Correction & Recovery)
Histogram Processing (Light1ng Balance)
Output: Decis1on- Ready Data
This pipeline transforms chaotic sensory input into structured data a robot can trust.

## Slide 13: From Data to Decision
Cleaner Images
Better Obstacle
Detection.
Restored Data
Accurate
Localization.
Balanced Light
Reliable Outdoor
twigation.
These mathematical foundations are not just image manipulation; they are the prerequisites for autonomous interaction with the physical world.