## Slide 1: The Challenge of Perception A physical object rarely appears ’perfectly’ to a camera lens. The real world is 3D and dynamic; the camera captures a static 2D slice. To a computer, a rotated cup is mathematically distinct from an upright cup.
Real World Object (3D)
Sensor Capture
Transformed Image (2D)
Gap: To bridge this perception gap, we use Image Transformations to mathematically
map and correct changes in rotation, translation, scale, and perspective.

## Slide 2: Geometric Image Transformations
150 | 128 | 192 | ] | 
[ 75 | 201 | 44 | ] | 
255 | 52 | 110 |  | ]
From Pixels to Pefspective: A Foundational Guide for Computer Vision & Robotics.

## Slide 3: The First Truth: An Image is Just a Grid of Values
-
To understand transformations, we must distinguish between two properties of a pixel:
1. Position: The coordinates (K, y).
2. Value: The intensity(e.g., 120 in
grayscale) or color (RGB).
The Golden Rule: Geometric transformations change the Position, never the Value.

## Slide 4: Cameras Capture a Distorted Reality When a robot sees an object, it rarely appears ”perfect.” The object might be rotated, shifted, zoomed, or viewed from an extreme angle. To track an object or map an environment, we must mathematically relate different views to the same physical object.
Real Obj ect (Phys1ca1 Truth)
Distortion
Camera Lens/Sensor
Trans fo rmed Isa ge (Came r a 0u t put )
Math /
Correction
Co r rected Image

## Slide 5: Level : Orthogonal Transformation
Rotation
Definition:
Moves pixels via
rotation or reflection (mirroring).
Reflection
Rotation Matrix
Constraints:
Shape, size, and
angles do NOT
change.
Distances are
preserved.
X ' = X COS(8) - y sin(8)
y' = x sin(B) + y oos(B)
Step 1: Potrait
Rotate 90°
Step 2: Landscape
Example: Screen rotation. The content
rotates, but the icon size is identical.

## Slide 6: Level 1: The Rigid World (Orthogonal)
The strictest form of movement. There is no size change and no distortion. The object simply
re-orients itself or flips.
„ :.. .
Real World Use
Correcting smartphone screen
orientation (Portrait/Landscape).
Rotation

## Slide 7: Tracing the Pixel: 9O° Rotation Logic

## Slide 8: Level Euclidean Transformation
Rotation + Translation (Shift)
x' = R[x] -r I

## Slide 9: Level The Rigid World in Motion (Euclidean)
We now allow the object to move through space (Translation). This models how solid objects behave in the physical world they turn and they move, but they don't deform.
Real World Use
Object Tracking (identifying a can
moving down a Jane).
Anchor Object
1
2
X

## Slide 10: Modeling Motion:Rotation + Translation
3â 6â 9â
2â 5â 8â
10 40 70
1. Rotate Final Result
3â 6â
2â 5â
1â 4â
Pixels shift right. New space becomes 0 (Black). Edge pixels are cropped.

## Slide 11: Rotation plus Translation
Rotation Matrix.
Handles orientation.
Translation Vector.
Handles position (x, y shift).
This equation combines the complex multiplication of the rotation matrix R with the simple addition of vector t. ENectively, it ‘spins’ the object first, then ‘picks it up’ to place it at a new coordinate.
Application: Navigation

## Slide 12: Level 3: Affine Transformation

## Slide 13: Level Stretching Reality (Affine)
We break the rigidity. Lines remain parallel, but angles and distances warp. This mimics mimics “shadow logic“ or viewing a flat surface from an angle.
Invar1ants
Parallelism (Parallel lines stay parallel)
Ratio of lengths on cotl1near po1nts
Real World Use
Correcting aerial photography taken from a tilted plane.
Scale —›
Anchor
Object
Shear —›

## Slide 14: Affine Mechanics: Scaling & Shearing
Scaling/Zoom
Scaling
(a=2,
d=2)
Shearing/Tilt
Shear1nq (x’ = x + y)
x’ = 2x, y’ = 2y.
Distance between pixels doubles.
Vertical lines tilt. Square becomes parallelogram.
Application: Residing images for Machine Learning or correcting camera tilt.

## Slide 15: Scale, Shear, and Tilt
Linear Transformation Matrix.
These four variables interact to control Scale (zooming) and Shear (slanting).
Translation Vector
(Position).
Unlike Orthogonal rotation, the variables a, b, c, d are not bound by sine or cosine. They can be any value, allowing the grid to stretch and skew.
Application: Calibration

## Slide 16: Level 4: Projective Transformation
Width: 20px

## Slide 17: Level 4: The Perspective Shift (Projective)
The most powerful transformation. It models how eyes and cameras actually work: parallel lines converge at a vanishing point.
Invariants
Straight lines nemain straight
Cross-ratio
WARNING: Parallel lines are NO LONGER
parallel.
Real World Use
Autonomous Driving (Lane Detection).
Vanishing Point X
Anchor
Object

## Slide 18: The Math of Perspective: The Homography Matrix
Division by w
Near
Object
(Small w)
Division by w
Large Output

## Slide 19: The Hierarchy of Power Comparing Transformation Complexity
Transformation | Action | Preserves Size? | Preserves Parallel Lines?
Orthogonal JetBrains Mono | Rotate / Mirror | YES | YES
Euclidean JetBrains Mono | Rotate + Shift | YES | YES
Affine JetBrains Nono | Scale + Tilt | NO | YES
Projective JetBrains Mono | Perspective | NO | N0 — Models 3D Depth
As we move down the list, the transformations become more powerful and closer to human vision, but the math becomes more complex.

## Slide 20: Key Takeaways
Orthogonal
Moves pixels via rotation/mirroring without changing values, shape,
or size.
Afiine
Maps pixels using linear scaling and shearing, allowing size/shape changes while preserving parallel lines.
Euclidean
Changes pixel position via rotation and translation while preserving size and shape.
Projective
The most general form; models 3D perspective where parallel lines converge and size changes with depth.

## Slide 21: The Foundation of Computer Vision
In the real world, the same object looks different from every angle.
Image transformations allow a robot to understand that these different
views still represent the same object.
“Transformations are the bridge between raw pixels and physical understanding.”